fluids.flow_meter.differential_pressure_meter_solver(D, rho, mu, k, D2=None, P1=None, P2=None, m=None, meter_type='ISO 5167 orifice', taps=None)
Calculates either the mass flow rate, the upstream pressure, the second pressure value, or the orifice diameter for a differential pressure flow meter based on the geometry of the meter, measured pressures of the meter, and the density, viscosity, and isentropic exponent of the fluid. This solves an equation iteratively to obtain the correct flow rate.
Parameters:	D : float / Upstream internal pipe diameter, [m] / rho : float / Density of fluid at P1, [kg/m^3] / mu : float / Viscosity of fluid at P1, [Pa*s] / k : float / Isentropic exponent of fluid, [-] / D2 : float, optional / Diameter of orifice, or venturi meter orifice, or flow tube orifice, or cone meter end diameter, or wedge meter fluid flow height, [m] / P1 : float, optional / Static pressure of fluid upstream of differential pressure meter at the cross-section of the pressure tap, [Pa] / P2 : float, optional / Static pressure of fluid downstream of differential pressure meter or at the prescribed location (varies by type of meter) [Pa] / m : float, optional / Mass flow rate of fluid through the flow meter, [kg/s] / meter_type : str, optional / One of (‘ISO 5167 orifice’, ‘long radius nozzle’, ‘ISA 1932 nozzle’, ‘venuri nozzle’, ‘as cast convergent venturi tube’, ‘machined convergent venturi tube’, ‘rough welded convergent venturi tube’, ‘cone meter’, ‘wedge meter’), [-] / taps : str, optional / The orientation of the taps; one of ‘corner’, ‘flange’, ‘D’, or ‘D/2’; applies for orifice meters only, [-]
Returns:	ans : float / One of m, the mass flow rate of the fluid; P1, the pressure upstream of the flow meter; P2, the second pressure tap’s value; and D2, the diameter of the measuring device; units of respectively, kg/s, Pa, Pa, or m

Notes
See the appropriate functions for the documentation for the formulas and references used in each method.
The solvers make some assumptions about the range of values answers may be in.
Note that the solver for the upstream pressure uses the provided values of density, viscosity and isentropic exponent; whereas these values all depend on pressure (albeit to a small extent). An outer loop should be added with pressure-dependent values calculated in it for maximum accuracy.
It would be possible to solve for the upstream pipe diameter, but there is no use for that functionality.